## Slide 1: E-Boom Introduction
Mark Trowman Product Development Manager EMEA

## Slide 3
Skyjack’s new range of battery powered
electric rough terrain articulated booms
have been developed to provide a clean, quiet,
sustainable rental solution with no emissions,
lower operating costs and increased utilisation.

## Slide 4
Available with 15.7 m (51 ft) and 20.1 m (66 ft) working heights
and suitable for indoor and outdoor use,
the SJ45 AJE+ and SJ60 AJE+ models include
High performance AC electric traction and pump motors
to deliver high torque power and consistent multi-function capability.

## Slide 5
Featuring many of the design features that you have come to expect from Skyjack
this new range remains simple, reliable and
provides an environmentally friendly and sustainable choice for rental.

## Slide 6
Rental companies and major contractors face increasing demands for sustainability information.
Skyjack has introduced its ECO mark to support our customers by providing products that deliver benefits in environmental performance and long-term sustainability

## Slide 8
AC Electric Drive

## Slide 9
      All electric, four-wheel, axle-based drive provides improved efficiency and rough terrain performance.

## Slide 10
      The drive system uses a high-performance AC induction traction motor and AC pump motor system to optimise current torque, power and speed.

## Slide 11
      An oscillating steer axle works in conjunction with the drive system to keep all four tires in contact with the ground, even in the roughest of terrains.
      Improved traction provides a noticeably smoother ride and consistent multi-function capability delivers a superior operator experience.

## Slide 12
      Skyjack’s SJ45 AJE+ and SJ60 AJE+ have been designed to meet true job site performance expectations, whether it be navigating various rough terrain conditions or platform capacities.
      Strategic placement of motors, batteries and controllers allow for accessibility and protection of parts.

## Slide 13
      Operator controlled locking rear differential and limited slip front differential.
      Drivable at full height.
      48V system.
      23A automatic battery charger with battery condition indicator.
        Charges to full in <15 hrs on 110V.
        “Bulk” Charge, 20-80% <9 hrs on 110V.
      415 Ah AGM batteries.
      Regenerative braking.

## Slide 14
      Zero emissions.
      Indoor and outdoor use.
      Work all day or night.
      Emission restricted areas.

## Slide 15
Machine Performance

## Slide 17: Duty Cycle and Efficiency
Exceptional duty cycle, providing a competitive edge without sacrificing performance.
Capable of supporting more than a typical full day’s use of machine.
Reserve operation:
  35% low level warning with no impact on working performance
  20% limp mode with battery protection and greater than 1 hours stowed drive time (at 3.2km/h) to allow travel charging point.
Unlike some other manufacturers Skyjack have maintained or improved:
  Improved drive performance - optimised current torque, power and speed.
  Indoor and outdoor use.
  Up to 454 kg platform capacities with same reach envelope as previous models.

## Slide 18
High Capacity

## Slide 19
Increases productivity.
Integrated with load sensing.
Lights on control box indicate zone, based on weight and position.
Capacities up to 454 kg (1000 lbs) and 3 persons in the platform.

## Slide 20
Controls

## Slide 21: Upper control box
Shares a similar layout with IC machines.
Engine, Fuel and Glow Plug lights are replaced with a Battery Status Indicator light
    100% to 35% - solid light is green, unrestricted operation.
    34% to 20% - low pulse light is amber, unrestricted operation.
    19% to 0% - fast pulse light is red, buzzer sounds for 1 second every 5 seconds, limited operation (no lifting, drive speed limited to 3.2 kmh).
Following switches are removed
    Engine start/on/off.
    Low/high throttle engine speed.
    Optional generator.

## Slide 22: Lower control box
Updated to accommodate engine power source change
  Hour meter has been replaced with new display that shows machine hours, state of charge and fault codes.
  Engine, glow plug, water in fuel and fuel lights removed
  Start/function enable/emergency power switch separated in to two separate switches
    start/enable and emergency power
  Electric brake release switch added, replacing hydraulic release system.

## Slide 23
Low Operating Costs

## Slide 24
  Skyjack’s electric booms provide
  additional low lifetime ownership
  and running costs
  Efficient maintenance free AGM batteries.
  No engine maintenance requirements
    No fuel liquid fuel systems, filters, emission control costs.
  Much easier for customers to use.
  Straightforward to maintain, service
    Less mechanic time.

## Slide 25
  Skyjack’s electric booms provide additional low
  lifetime ownership and running costs
  Commonality of parts between E-boom models.
  Common machine architecture of parts with existing boom models (Diesel).

## Slide 26
Unique to Skyjack

## Slide 27
Skyjack’s colour coded and numbered wiring system makes our machines the easiest to troubleshoot and repair.

## Slide 28
True axle-based four-wheel drive gives positive traction and excellent rough ground terrainability.

## Slide 29
Keeps boom drive controls in the orientation of the boom regardless of position of the turret over chassis.

## Slide 30
Cycles between max height and ground level quickly by engaging only the boom raise/lower function.

## Slide 31
Ensures that the riser and main pivot point connecting the fly boom to the riser travel in a straight vertical line.

## Slide 33
Thank You